## Slide 1: 完全基于发动机结构的发动机控制策略设计
核心出发点
按照发动机的构造来建立各个系统，以兼容汽油和柴油发动机
其它
1. 实现更准确的瞬态控制
2. 只要懂发动机的人就能理解控制策略
3. 能更好地利用CAE技术来优化模型和控制
4. 便于功能的扩展，很容易找到新功能应该介入的位置
Colin Zhou 20180425

## Slide 2: 完全基于发动机结构的发动机控制策略设计
发动机结构
曲柄连杆机构
配气机构
燃料供给系统
冷却系统
润滑系统
点火系统
起动系统
进气系统
排气系统
Engine System
Crank train Parts
Timing System
Fuel System
Coolant System
Oil System
Ignition System
Start System
AirIn System
Exh System
Chamber Model
Electric Power Supply System
Crank Case Ventilation System
EGR System
Colin Zhou 20180425

## Slide 3: 完全基于发动机结构的发动机控制策略设计
Sensor Layer
Model&Control Layer
Actuator Layer
Colin Zhou 20180425
Crank Train Parts
Timing System
Fuel System
Coolant System
…………
Engine
Vehicle
Power Train System
Driver System
…………

## Slide 4: 完全基于发动机结构的发动机控制策略设计
Colin Zhou 20180425
系统(system)由部件(component)组成
Model Layer
Filter
Comp
IC
Throt

## Slide 5: 完全基于发动机结构的发动机控制策略设计
Colin Zhou 20180425
命名规则
AirIn_pAir_uFilter
AirIn_TAir_dIC
AirIn_dmAir_dThrot
AirIn_rEGR_uPort
System Name
Parameter,P-Pressure, T-Temperature, dm-mass flow, r-rate
work medium, like air, coolant, fuel
d-down stream, u-up stream
Component Name